## Slide 1: Visualization of multi-axis ultrasonic scanning route simulation for curved parts
Instructor：Yang Zhang
Student：Zizhuo Wang and others

## Slide 2
Background
1
2
3
4
Reconstruction of curved parts
Scanning path planning
Coordinate matching and visualization
5
Summary
Contents

## Slide 3: Background
01

## Slide 4
1.1 requirement of aviation surface scanning
The usage of sculptured surfaced parts has been increasing in multiple areas like aerospace or medical equipment.
The precision of defect detection is required, for example in airplanes.
Engine blade
Radar cover
C919
Requirement: scanning curves in a plane requires high precision, high stability and high efficiency.

## Slide 5
1.2 Methods of aviation surface scanning
A Six axis robotic arm ultrasonic scanning system with guide rail is used in this project to conduct nondestructive test of parts with sculptured surface.
Working principal of ultrasonic detection
Robot arm scanning system with guide rail
Strong penetration, high sensitivity to defects such as interlayers and cracks;
Safe to manipulate
High degree of freedom, capability of detecting workpieces with sculptured surface;
Strong applicability

## Slide 6: Reconstruction of curved parts
02

## Slide 7
2.1 Literature research and scheme selection
Research content in the field of reconstruction
Reconstruction methods
Triangular reconstruction
NURBS curves and surfaces
B-spline curves and surfaces
Coons surface
Bezier curves and surfaces
application
development
aerospace
Shipbuilding
Design process
other
Algorithm simplification
Math achievements application
Multiple algorithm fushion
Blade, gauge skin
Blade, hull
Modelling software

## Slide 8
Work flow
Reconstruction of Cross-sectional line
Reconstruction of surface
Analysis of reconstructed surface
Test data: head gauge skin of a large aircraft
2.1 Literature research and scheme selection

## Slide 9
2.2 Reconstruction of Cross-sectional line
Program structure of reconstruction
Parameterization
uniform
Corrected chord
chord
Boundary condition
Close curve
Open curve
Solve chord length
Input data
Assign parameters
Add boundary condition
Solve control points
Solve NURBS curve
generate curve
Data point coordinate
Node vector
Control point
NURBS curve
Direct
solve
Back
solve
parameterize
Solve control point
Solve curve

## Slide 10
Result of cross-sectional line reconstruction with sample curve
2.2 Reconstruction of Cross-sectional line

## Slide 11
2.3 Reconstruction of surface
Main method：A surface is an extension of curves.
View reconstructed curves as data points
Program structure of surface reconstructure
Data input
Main function
Solve chord
Apply parameter
Apply boundary condition
Solve control
points
Ergodic u and v
Generate figure
Figure function
Control point function
Parameterize function

## Slide 12
Result of reconstruction of sample surface
2.3 Reconstruction of surface

## Slide 13
2.4 analysis of reconstructed surface
Model matching with ICP
Distance calculation
Analysis
Error of reconstructed surface and real surface
Error: 0.19%

## Slide 14: Scanning path planning
03

## Slide 15
3.1 sampling method of test point —— step length
d1
d2
L
W
Circular probe
Rectangular probe
To increase scanning efficiency, step length takes the maximum which is determined by shape of the probe.

## Slide 16
3.1 sampling method of test point
Equal parameter
Parallel section
Advantage: convenient, easy to apply
Disadvantage: high demand of part shape, unequal step length
A series of cross-section lines is obtained by equally divide surface parameter along one direction
Intersects a series of parallel planes and test surface. The intersection points are test points
Method chosen：equal arc method

## Slide 17
3.1 sampling method of test point —— equal arc
Equal arc
Equal parameter
Dense equal parameter discretization
Find the interval of equal parameter points with arc and functions
Linear interpolation base on interval endpoints
Solve test point coordinates with equal arc parameters

## Slide 18
Result of discretization of sample lines
3.1 sampling method of test point —— equal arc

## Slide 19
3.2 Method of path planning
Surface equal parameter discretization
Curve reconstruction on U direction
Equal arc separation
Curve reconstruction on V direction
Solve nearest point
Get data points by discretization the surface;
Reconstruct data points into curves along U direction;
Equal arc separates reconstructed curves to get data point with equal arc along U direction;
Reconstruct these points along V direction into B-spline curves;
Equal arc separates B-spline curves.
Find nearest data points of the generated points, get equal arc point coordinates and parameters.

## Slide 20
3.2 method of path planning——determine attitude
Mapping relationship between points on surface and points in parameter field
n
Solve normal vector:

## Slide 21
1
2
3
4
5
6
3.2 method of path planning——result

## Slide 22
Set parameters like arc length and search accuracy
Input surface control points and node matrices
3.2 method of path planning——program structure
Set parameters
Reconstruct surface
Equal chord sample
Array path points
Main function
Input module
output
Display path
Display points
Display surface
Display module

## Slide 23
3.3 Simulation test
Reconstruct surface
Solve equal chord points
Solve path and posture
Length (distance between curves) /mm | Width（distance between points）/mm | Total mesure points
66×0.8 | 39×0.8 | 558
Chord parameter

## Slide 24
3.3 Simulation test —— scanning simulation
joint |  |  |  |  | Joint range/()
1 | 100 | -90 | 615 |  | -180~180
2 | 705 | 0 | 0 |  | -100~110
3 | 135 | -90 | 0 |  | -60~65
4 | 0 | 90 | 755 |  | -200~200
5 | 0 | 90 | 0 |  | -120~120
6 | 0 | 0 | 85 |  | -400~400
joint |  |  |  |  | 
1 | 100 | -90 | 615 |  | -180~180
2 | 705 | 0 | 0 |  | -100~110
3 | 135 | -90 | 0 |  | -60~65
4 | 0 | 90 | 755 |  | -200~200
5 | 0 | 90 | 0 |  | -120~120
6 | 0 | 0 | 85 |  | -400~400
Parameters of IRB 2400 D-H
IRB2400
Establish arm model

## Slide 25
3.3 Simulation test —— scanning simulation
Transform path and attitude coordinates and input into MATLAB simulation environment.
The result of planned scanned path shows as follow:
Scanning path points of robot arm
Posture change of some joints

## Slide 26: Coordinate matching and visualization
04

## Slide 27
4.1 Matching method of coordinates
The scanning process requires repeated scanning of multiple parts with same appearance.
The procedure of sampling, reconstructing and path generating is carried out repeatedly because of repeated clamping and incomplete clamping.
With the help of point cloud matching method, fewer sample point can accomplish the relocation of scanning path.
Rotation matrix and translation matrix are solved and the error becomes minimal when Q = R * P + t.

## Slide 28
4.1 Matching method of coordinates
Rough matching method: Principal Component Analysis (PCA)
Method: To solve principal axis of the point clouds and match their direction.
Advantage: Can roughly match two point clouds with rather high speed.
Disadvantage: Matching precision is rather low.
Before PCA
After PCA

## Slide 29
4.1 Matching method of coordinates
After PCA
After ICP
Precise matching method: iterative closest point (ICP)
For every point ax in point cloud A, the closest point bx in cloud B is found. The two point clouds are matched so that error Ex is minimal.
This process is repeated until E becomes minimal.
Advantage: Matching precision is high.
Disadvantage: Time consumption is rather high and may
Result in local optimal solution.

## Slide 30
Disadvantage of ICP
ICP result Without PCA
ICP result With PCA
error
error
4.1 Matching method of coordinates

## Slide 31
Choosing method of sample points
In general：
（1）Distance between sample
points should be as large as possible.
（2）Unilateral triangles should be chosen.
When conducting coordinates matching:
Points with obvious geometric feature (larger curvature) should be chosen.
25 points are chosen to satisfy both sampling speed and error range.
Number of sample points
Matching error
4.1 Matching method of coordinates

## Slide 32
4.2 visualization of scanning path

## Slide 33
4.3 simulation experiment based on head gauge skin of a large aircraft
Iterated 18 times until error reduced to 0.97

## Slide 34: Summary
05

## Slide 35
5 Summary
Goal
Used NURBS curve and surface reconstruction
Method
Finished reconstruction of free-form prats as planned, with evaluated quality being acceptable.
Lack of data prepossessing and physical experiment.
Result
To establish a surface model based on point clouds and evaluate reconstruction quality.
Reconstruction of curved parts

## Slide 36
5 Summary
Goal
Generated sample points with equal chord method and zig-zag scanning.
Method
Finished path planning with equal chord method as planned, and the result path meets primary goals.
Calculation efficiency can be increased.
Time complexity can be reduced.
Program structure can be optimized.
Result
To solve a path with reliable and complete result.
To reduce test points and increase efficiency.
Scanning path planning

## Slide 37
5 Summary
Goal
Combinatorial algorithm including PCA and ICP;
Visualization and simulation software made with qt.
Method
Achieved coordinate matching as planned;
Scanning path point cloud displayed and scanning process simulated.
ICP method can be optimized.
Visualization software requires more modules and display modes.
Lack of physical experiment.
Result
To match coordinate of scanning path and robot movement;
To accomplish visualization and simulation of the scanning path.
Coordinate matching and visualization

## Slide 38
Thank you for listening!